# Skeleton Parser 2009 (Beta V0.1.0.1)
## Introduction
The ISPF Skeleton Parser reads file tailoring input files (skeletons) and generates several cross-reference files:
- Skeleton file-to-variable cross-reference
- Skeleton file-to-embedded skeleton file cross-reference
- Skeleton file-to-ISPF skeleton built-in function cross-reference

For each cross-reference dataset, three optional file formats can be created:
- XML records
- Comma separated value records, suitable for loading into an Excel spreadsheet
- Fixed format records, suitable for loading into relational tables.

This version of the parser is not an update to any previous version. At present there is a limited graphic user interface front-end. The parser itself runs as a command-prompt .exe file and it is invoked internally by the graphic front-end.
## Installation
There are two installation files:
- SETUP.EXE
- INSTALLER.MSI

You must have administrator rights to the system on which you will be installing the parser. Also, you must have the right to install applications.
To install the parser, simply run the setup program. Note that this program will install the Microsoft .NET 3.5 run time. This run time will be downloaded from Microsoft, therefore the installer needs Internet access. It is the installation of the .NET run time that requires administrator rights on your PC.
Following the run time installation the SETUP.EXE program will install the parser and its supporting files. You will be able to override the default install destination directory. The rest of the installation is automated. All of the installation files related to the utility (save for the .NET run time) are installed in a single directory.
The application directory installed files are:

Config1.xml	A sample XML file. You can use this as a base copy. If you	accidentally wipe out the base copy there is a backup in the	Samples directory.

imbeds2.ico	The icon for the uninstaller
Library.dll	Program support library
LibraryConcatenation.dll	Program support library
Parser.dll	Program support library
README.TXT	Updated program information.
SkeletonParserDS.dll	Program support library
SkeletonParser.exe	The parser program.
SkeletonParserQuery.exe	The Graphical Front End for the parser engine (see below). This is	a GUI query program for displaying the Skeleton-Variable cross	reference, Skeleton-Skeleton cross-reference and the Skeleton	Expansion as table data.
SkelParser.cmd	A sample CMD file to invoke the parser program.
Utility.dll	Program support library
XMLParmsReader.dll	Program support library

Below the application directory are two other directories, Samples and Doc. This documentation is in the Doc directory:
SkeletonParser_Readme.PDF	This documentation.

The Samples directory installed files are:
BASE.xml	A read only sample XML parameters file. This should not be	modified, but can be copied to create new configurations.
BASE.xsd	A read only schema for the XML file
parser.rex	A sample Regina REXX program showing how to parse the	program output.
parserDB2.rex	A sample Regina REXX program showing how to parse the fields	offsets fixed format file to create DB2 CREATE TABLE control	cards.
SkelParserDB2R.cmd	Invokes parserDB2.rex, passing in a configuration XML file	name.
SkelParserR.cmd	Invokes parser.rex, passing in a configuration XML file name.

## The Parser Engine
The parser.dll file implements the parser engine. The engine does the actual analysis of skeleton data passed in the XML parameter file. The parser engine generates internal data stores that are then used to create the various output or query data defined below. The parser engine can be invoked by the batch parser and the Graphical Front End (GFE).
## Customization
You must create a separate directory on the target PC system for each host PDS. There must be one dataset for each member of the PDS. At this time, no utilities are supplied to facilitate transferring files from the z/OS host to the PC.
The parser supports multiple host PDS concatenations. Each unique concatenation of datasets must be specified in a separate XML file. A sample XML file has been provided for customization. This is Config1.xml. Config1.xml is a copy of Base.xml. Note that Config1.xml and Base.xml are identical, but BASE.XML is marked READONLY. You should leave BASE.XML as a model for any configurations you want to create. But if you copy BASE.XML, be sure to change the file properties of the newly created file to remove the READONLY property.
## XML Tags
### <QueryDisplayName>
A character string that is used in the Graphical Front End Query GUI to identify the configuration on all of the dialog windows. Note that this does not have to match the <ConfigurationName> value described below in the fixed file output tags definitions.
### <Directory>
Find the <Directory> tag. In BASE.XML it is:

<Directory>
    <DirectoryName>C:\mypath\mycustomSkels</DirectoryName>
    <DirectoryLabel>Custom</DirectoryLabel>
    <DirectoryHostName>somnode.CUSTOM.SKELS</DirectoryHostName>
  </Directory>
  <Directory>
    <DirectoryName>C:\mypath\myvendorSkels</DirectoryName>
    <DirectoryLabel>Vendor</DirectoryLabel>
    <DirectoryHostName>somnode.VENDOR.SKELS</DirectoryHostName>
  </Directory>
You may specify one or more directories. Each represents one host ISPF skeleton PDS. The order of the <Directory> tags should match the order of the concatenation that is being simulated. The above XML fragment represents this JCL:

//ISPSLIB DD DISP=SHR,DSN=somnode.CUSTOM.SKELS
// DD DISP=SHR,DSN=somnode.VENDOR.SKELS
### <DirectoryName>
This is the PC directory containing the datasets copied from one host PDS. At the time the parser is run, this directory must exist, or the parser will terminate with an error. The directory does not have to be on the C: drive, and it can be on a network drive that is read accessible. Note that reading files in network folders from a parser running on a remote machine will be a slower process.
### <DirectoryLabel>
The directory labels are not critical to the program operation. They are written as specified to one of the output files. The label is just a way to give a more meaningful title to the specified Host/PC file combination in the <Directory> element.
### <DirectoryHostName>
Like the <DirectoryLabel>, the data supplied for the <DirectoryHostName> is not critical to the program operation. It is useful for identifying what host file was used to fill the members in the PC directory.
### Output file types
There are three output file types: CSV (comma separated values), XML and fixed format. Within each of the file types there are several output datasets:
#### Variables
The Variables dataset contains fields showing the Skeleton-Variable relationships.
#### Skeletons
The Skeletons dataset contains fields showing the Skeleton-)IM'd skeleton relationships.
#### Tables(DOT)
The DOT dataset contains fields showing the Skeleton-)DOT (table) relationships.
#### Functions
Each function is shown in the Variables reference. But the Functions dataset contains extra information, showing the arguments passed to each function.
#### Libraries
The information in the Libraries file is directly extracted from the XML <Directory> elements in your input.
#### Keywords
For the fixed format file output, the Keywords file contains information that can be used to build a look-up table. Most keywords are ISPF Skeleton commands, such as IM, SEL, SET or DO. But there are some that further delineate some of the commands. Thus DOWHILE and DOUNTIL are refinements to how a )DO statement can be written, but neither DOWHILE nor DOUNTIL are ISPF commands.
The non-ISPF keywords are: DOWHILE, DOUNTIL and DATALINE.
#### VarTypes
The VarTypes dataset is a lookup table for variable type numbers used in the Variables dataset. This dataset is only generated if the fixed format output files are generated.
VARIABLE_REFERENCE
Variable found in a non-command line.
CONSTANT_REFERENCE
A constant found in a )SET or )SETF statement. Up to the first eight characters are shown.
CONSTANT_TEST
A constant found in a )SEL or )IF statement. Up to the first eight	characters are shown.
VARIABLE_TEST
A variable used in a )SEL or )IF statement
LVAL_ASSIGNMENT
The left side (LVAL) of an assignment statement, )SET or )SETF. The variable is specified	without a leading &.
LVAL_INDIRECT_ASSIGNMENT
The left side (LVAL) of an assignment statement, )SET or )SETF. The variable name has a	leading &, so it is an indirect assignment. For example:
)SET FRED = ETHEL
)CM The following is the same as )SET ETHEL = 3
)SET &FRED = 3

RVAL_CONSTANT_ASSIGNMENT
The right side (RVAL) of an assignment statement is a constant.
RVAL_VARIABLE_ASSIGNMENT
The right side (RVAL) of an assignment statement is a variable.
LVAL_NULL_ASSIGNMENT
The )SET or )SETF statement is a null (&Z) assignment. The LVAL variable has no leading &.
LVAL_INDIRECT_NULL_ASSIGNMENT
The )SET or )SETF statement is a null (&Z) assignment. The LVAL is indirect (variable	name has a leading &).
REXX_CALL_CONSTANT_REFERENCE
A constant used in an in stream )REXX statement.
REXX_CALL_VARIABLE_REFERENCE
A variable used in an in stream )REXX statement.
REXX_PROCEDURE
An external procedure specified in a )REXX statement
FUNCTION
The listed variable is an ISPF skeleton built-in function.
#### FieldOffsets
The FieldOffsets file is only generated for fixed format output. It contains the field names, types and offsets of the data in each file. This file can be used to generate load datasets for relational databases.
Table: Variables
....+....0....+....0....+....0....+....0....+....0....+....0....+....0....+....0
Configuration 001 030 030 String False
ConfigNum 031 005 002 Int16 False
Variable 036 072 072 String False
Skeleton 108 008 008 String False
LineNumber 116 006 004 Int32 False
Position 122 005 002 Int16 False
Command 127 009 009 String False
CommandCode 136 005 002 Int16 False
Type 141 030 030 String False
TypeCode 171 005 002 Int16 False
Table: Skeletons
....+....0....+....0....+....0....+....0....+....0....+....0....+....0....+....0
Configuration 001 030 030 String False
ConfigNum 031 005 002 Int16 False
Skeleton 036 008 008 String False
SkelOffset 044 005 002 Int16 False
ChildSkeleton 049 025 025 String False
ChildSkelOffset 074 005 002 Int16 False
LineNumber 079 006 004 Int32 False
OPT 085 001 001 Boolean False
NOFT 086 001 001 Boolean False
EXT 087 001 001 Boolean False
Table: Functions
....+....0....+....0....+....0....+....0....+....0....+....0....+....0....+....0
Configuration 001 030 030 String False
ConfigNum 031 005 002 Int16 False
Function 036 008 008 String False
Skeleton 044 008 008 String False
LineNumber 052 006 004 Int32 False
Position 058 005 002 Int16 False
Argument 063 060 060 String False
Table: Libraries
....+....0....+....0....+....0....+....0....+....0....+....0....+....0....+....0
Configuration 001 030 030 String False
ConfigNum 031 005 002 Int16 False
Offset 036 005 002 Int16 False
UserTag 041 050 050 String False
HostFileName 091 044 044 String False
PCFileName 135 256 256 String False
Table: Keywords
....+....0....+....0....+....0....+....0....+....0....+....0....+....0....+....0
CommandCode 001 005 002 Int16 True
Command 006 020 020 String False
Table: VarTypes
....+....0....+....0....+....0....+....0....+....0....+....0....+....0....+....0
TypeCode 001 005 002 Int16 True
Type 006 030 030 String False
Table: Configurations
....+....0....+....0....+....0....+....0....+....0....+....0....+....0....+....0
ConfigNum 001 005 002 Int16 True
Configuration 006 030 030 String False
Table: DOT
....+....0....+....0....+....0....+....0....+....0....+....0....+....0....+....0
Configuration 001 030 030 String False
ConfigNum 031 005 002 Int16 False
Skeleton 036 008 008 String False
TableName 044 030 030 String False
LineNumber 074 006 004 Int32 False
Table: Programs
....+....0....+....0....+....0....+....0....+....0....+....0....+....0....+....0
Configuration 001 030 030 String False
ConfigNum 031 005 002 Int16 False
Skeleton 036 008 008 String False
ProgramName 044 030 030 String False
LineNumber 074 006 004 Int32 False

 The table names are only suggestions. They match the generated low level qualifier of the above specified output file names. The fields in the file are defined thus:

Column	Length / Type	Description
1	32 / character	Field Name
34	3 / numeric	Offset (first field is always at offset 1)
38	3 / numeric	Display length
42	3 / numeric	Internal length
46	15 / Character	Type / Int16 = 2 byte integer / Int32 = 4 byte integer / String = variable length character string.
62	5	Key field indicator (True or False)

See the sample Rexx file ParserDB2.REX. This Regina Rexx program processes the above offsets file to create z/OS DB2 DDL and utility LOAD statements.
### <ExcelOutput>

<ExcelOutput>
    <ExcelOutputFolder>C:\myCSVOutputPath\</ExcelOutputFolder>
    <ExcelOutputHLQ>cProd</ExcelOutputHLQ>
  </ExcelOutput>

Use the <ExcelOutput> element to define the characteristics of a set of output files consisting of comma separated values (CSV). These files can be loaded into a spreadsheet program, such as MS Excel. If this element is not defined, then no CSV files will be generated or written.

The ExcelOutput related tags are ignored when the XML file is used as the control for the Graphical User Interface.
### <ExcelOutputFolder>
Use this element to define the full path to the directory in which the files will be generated. At the time the parser is run this directory must exist or the parser will terminate with an error.
As noted above, the ExcelOutput related tags are ignored when the XML file is used as the control for the Graphical User Interface.
### <ExcelOutputHLQ>
Use this element to define the High Level Qualifier(HLQ) of the CSV output datasets. To this HLQ will be appended one of the output dataset types: Variables, Skeletons, Tables (DOT), Programs (skeleton to executed program cross reference), Functions or Libraries. The Keywords, VarTypes and FieldOffset files are not generated for CSV output. For the output folder and HLQ shown above, the following files would be generated in the directory C:\myCSVOutputPath
cProd.Variables.csv
cProd.Skeletons.csv
cProd.DOT.csv
cProd.Programs.csv
cProd.Functions.csv
cProd.Libraries.csv

As noted above, the ExcelOutput related tags are ignored when the XML file is used as the control for the Graphical User Interface.
### <XMLOutput>

<XMLOutput>
    <XMLOutputFolder>C:\myXMLOutputPath</XMLOutputFolder>
    <XMLOutputHLQ>xProd</XMLOutputHLQ>
  </XMLOutput>

Use the <XMLOutput> element to define the characteristics of a set of output files consisting of XML tags for the parsed data. Some databases can be defined with XML file input. Newer languages can directly query data in XML files.

The XMLOutput related tags are ignored when the XML file is used as the control for the Graphical User Interface.
### <XMLOutputFolder>
Use this element to define the full path to the directory in which the files will be generated. At the time the parser is run, this directory must exist, or the parser will terminate with an error.
As noted above, the XMLOutput related tags are ignored when the XML file is used as the control for the Graphical User Interface.
### <XMLOutputHLQ>
Use this element to define the High Level Qualifier(HLQ) of the XML output datasets. To this HLQ will be appended one of the output dataset types: Variables, Skeletons, Tables (DOT), Programs (skeleton to executed program cross reference), Functions or Libraries. The Keywords, VarTypes and FieldOffset files are not generated for XML output. For the output folder and HLQ shown above, the following files would be generated in the directory C:\myCSVOutputPath
xProd.Variables.xml
xProd.Skeletons.xml
xProd.DOT.xml
xProd.Programs.xml
xProd.Functions.xml
xProd.Libraries.xml
As noted above, the XMLOutput related tags are ignored when the XML file is used as the control for the Graphical User Interface.
### <FixedOutput>

  <FixedOutput>
    <Configuration>
      <ConfigurationName>MyConfigName</ConfigurationName>
      <ConfigurationNumber>1</ConfigurationNumber>
    </Configuration>

    <FixedOutputFolder>C:\myFixedFilesOutputPath</FixedOutputFolder>
    <FixedOutputHLQ>fProd</FixedOutputHLQ>
  </FixedOutput>

Use this compound element to define the characteristics of a set of output files that can be used to load tables for a relational database such as DB2 or MS SQL Server.

Only the ConfigurationName and ConfigurationNumber tags are used when the XML file is used as the control for the Graphical User Interface. The FixedOutput related file and folder tags are ignored when the XML file is used as the control for the Graphical User Interface.

### <ConfigurationName> <ConfigurationNumber>
The reason for generating the fixed file input is create data to load relational database tables. The configuration name and number exist to allow output from different runs of the parser to be stored in the same tables. Use the Configuration data to retrieve the proper data for the concatenations you defined.

This might be clearer with an example.
If you have a test system with a test skeletons library and then a production skeletons concatenated following it, you can define a test configuration thus:

  <Directory>
    <DirectoryName>C:\mypath\test</DirectoryName>
    <DirectoryLabel>Custom</DirectoryLabel>
    <DirectoryHostName>P.CUSTOM.SKELS</DirectoryHostName>
  </Directory>
  <Directory>
    <DirectoryName>C:\mypath\vendor</DirectoryName>
    <DirectoryLabel>Vendor</DirectoryLabel>
    <DirectoryHostName>P.VENDOR.SKELS</DirectoryHostName>
  </Directory>
⋮
  <FixedOutput>
    <Configuration>
      <ConfigurationName>Test</ConfigurationName>
      <ConfigurationNumber>2</ConfigurationNumber>
    </Configuration>

    <FixedOutputFolder>C:\myFixedFilesOutputPath</FixedOutputFolder>
    <FixedOutputHLQ>fTest</FixedOutputHLQ>
  </FixedOutput>

With a production system that only uses the production library, the XML for the configuration would look thus:

  <Directory>
    <DirectoryName>C:\mypath\vendor</DirectoryName>
    <DirectoryLabel>Vendor</DirectoryLabel>
    <DirectoryHostName>P.VENDOR.SKELS</DirectoryHostName>
  </Directory>
⋮
  <FixedOutput>
    <Configuration>
      <ConfigurationName>Production</ConfigurationName>
      <ConfigurationNumber>1</ConfigurationNumber>
    </Configuration>

    <FixedOutputFolder>C:\myFixedFilesOutputPath</FixedOutputFolder>
    <FixedOutputHLQ>fProd</FixedOutputHLQ>
  </FixedOutput>

Note that the test and production configurations share an output folder, but that the HLQs of test and prod keep the output files distinct.
### <FixedOutputFolder>
Use this element to define the full path to the directory in which the files will be generated. At the time the parser is run, this directory must exist, or the parser will terminate with an error.
As noted above, the FixedOutput related file and folder tags are ignored when the XML file is used as the control for the Graphical User Interface.
### <FixedOutputHLQ>
Use this element to define the High Level Qualifier(HLQ) of the fixed output datasets. To this HLQ will be appended one of the output dataset types: Variables, Skeletons, Tables (DOT), Programs (skeleton to executed program cross reference), Functions, Libraries, Keywords, VarTypes and FieldOffsets. For the output folder and HLQ shown above, the following files would be generated in the directory C:\myFixedFilesOutputPath
fProd.Variables.txt
fProd.Skeletons.txt
fProd.DOT.txt
fProd.Programs.txt
fProd.Functions.txt
fProd.Libraries.txt
fProd.Keywords.txt
fProd.VarTypes.txt
fProd.FileOffsets.txt

As noted above, the FixedOutput related file and folder tags are ignored when the XML file is used as the control for the Graphical User Interface.
### <IgnoreSkel>
You may specify zero, one or more skeleton names that are to be ignored in the parsing. Use one <IgnoreSkel> element per skeleton. Only specify the eight character skeleton name, not the extension. The utility ignores file extensions.
### <Unimbedded Skeleton>
You may specify zero, one or more skeletons that are to be added to the Skeleton-to-Skeleton cross reference table. These skeletons are normally shown in the table as being )IM'd by “no parent”. You can change the parent to the name of a process or program, which would otherwise be unknown by the parser.
<Unimbedded Skeleton="CMN$$AUD" Parent="..AUDIT Program"/>
<Unimbedded Skeleton="CMN$$AUD" Parent="..AUDIT Program"/>
<Unimbedded Skeleton="CMNIMRPM" Parent="..PROMOTION"/>
<Unimbedded Skeleton="CMNIMPRM" Parent="..PROMOTION"/>
<Unimbedded Skeleton="CMN$$D2J" Parent="..DB2Jobs" NOFT="false" OPT="false" EXT="false"/>
<Unimbedded Skeleton="CMN$$OTH" Parent="LIBTYPE_OTHER" NOFT="false" OPT="false" EXT="false"/>
<Unimbedded Skeleton="CMN10" Parent="..Distribution" NOFT="false" OPT="false" EXT="false"/>
<Unimbedded Skeleton="CMN11" Parent="..Distribution" NOFT="false" OPT="false" EXT="false"/>
<Unimbedded Skeleton="CMN14" Parent="..Distribution" NOFT="false" OPT="false" EXT="false"/>
<Unimbedded Skeleton="CMN15" Parent="..Distribution" NOFT="false" OPT="false" EXT="false"/>
<Unimbedded Skeleton="CMN17" Parent="..Distribution" NOFT="false" OPT="false" EXT="false"/>
<Unimbedded Skeleton="CMN18" Parent="..Distribution" NOFT="false" OPT="false" EXT="false"/>
<Unimbedded Skeleton="CMN19" Parent="..Distribution" NOFT="false" OPT="false" EXT="false"/>
<Unimbedded Skeleton="CMN20" Parent="..Install" NOFT="false" OPT="false" EXT="false"/>
<Unimbedded Skeleton="CMN20I" Parent="..Install" NOFT="false" OPT="false" EXT="false"/>
<Unimbedded Skeleton="CMN21" Parent="..Install" NOFT="false" OPT="false" EXT="false"/>
<Unimbedded Skeleton="CMN24" Parent="..Install" NOFT="false" OPT="false" EXT="false"/>
<Unimbedded Skeleton="CMN25" Parent="..Install" NOFT="false" OPT="false" EXT="false"/>
<Unimbedded Skeleton="CMN28" Parent="..Install" NOFT="false" OPT="false" EXT="false"/>
<Unimbedded Skeleton="CMN29" Parent="..Install" NOFT="false" OPT="false" EXT="false"/>
<Unimbedded Skeleton="CMN30" Parent="..Baseline" NOFT="false" OPT="false" EXT="false"/>
<Unimbedded Skeleton="CMN30I" Parent="..Baseline" NOFT="false" OPT="false" EXT="false"/>
<Unimbedded Skeleton="CMN31T" Parent="..Temp" NOFT="false" OPT="false" EXT="false"/>
<Unimbedded Skeleton="CMN31TI" Parent="..Temp" NOFT="false" OPT="false" EXT="false"/>
<Unimbedded Skeleton="CMN32" Parent="..Baseline" NOFT="false" OPT="false" EXT="false"/>
<Unimbedded Skeleton="CMN34T" Parent="..Temp" NOFT="false" OPT="false" EXT="false"/>
<Unimbedded Skeleton="CMN35T" Parent="..Temp" NOFT="false" OPT="false" EXT="false"/>
<Unimbedded Skeleton="CMN37" Parent="..Baseline" NOFT="false" OPT="false" EXT="false"/>
<Unimbedded Skeleton="CMN38T" Parent="..Temp" NOFT="false" OPT="false" EXT="false"/>
<Unimbedded Skeleton="CMN39T" Parent="..Temp" NOFT="false" OPT="false" EXT="false"/>
<Unimbedded Skeleton="CMN49" Parent="..Backout" NOFT="false" OPT="false" EXT="false"/>
<Unimbedded Skeleton="CMN50" Parent="..Backout" NOFT="false" OPT="false" EXT="false"/>
<Unimbedded Skeleton="CMN50I" Parent="..Backout" NOFT="false" OPT="false" EXT="false"/>
<Unimbedded Skeleton="CMN50T" Parent="..TempBkout" NOFT="false" OPT="false" EXT="false"/>
<Unimbedded Skeleton="CMN50TI" Parent="..TempBkout" NOFT="false" OPT="false" EXT="false"/>
<Unimbedded Skeleton="CMN51" Parent="..Backout" NOFT="false" OPT="false" EXT="false"/>
<Unimbedded Skeleton="CMN54" Parent="..Backout" NOFT="false" OPT="false" EXT="false"/>
<Unimbedded Skeleton="CMN55" Parent="..Backout" NOFT="false" OPT="false" EXT="false"/>
<Unimbedded Skeleton="CMN55I" Parent="..Backout" NOFT="false" OPT="false" EXT="false"/>
<Unimbedded Skeleton="CMN55T" Parent="..TempBkout" NOFT="false" OPT="false" EXT="false"/>
<Unimbedded Skeleton="CMN55TI" Parent="..TempBkout" NOFT="false" OPT="false" EXT="false"/>
<Unimbedded Skeleton="CMN56" Parent="..Backout" NOFT="false" OPT="false" EXT="false"/>
<Unimbedded Skeleton="CMN57" Parent="..Backout" NOFT="false" OPT="false" EXT="false"/>
<Unimbedded Skeleton="CMN58" Parent="..Backout" NOFT="false" OPT="false" EXT="false"/>
<Unimbedded Skeleton="CMN59" Parent="..Backout" NOFT="false" OPT="false" EXT="false"/>
<Unimbedded Skeleton="CMN64" Parent="..Revert" NOFT="false" OPT="false" EXT="false"/>

The Unimbedded element has five attributes: Skeleton, Parent, NOFT, OPT and EXT. The Skeleton is the name of a skeleton that is not )IM'd by any other skeleton in the concatenation. The Parent is the name of a process or dialog that uses the ISPF FTINCL to invoke the skeleton. You may specify up to 40 characters here. If longer strings are specified, they are truncated to 40 characters. NOFT, OPT and EXT are the file tailoring options for “no file tailoring”, “optional” and “extend ON”. These have either a true or a false value. The default is false.
The Unimbedded element must have at the minimum a Skeleton and a Parent attribute, or the XML configuration file will be rejected. If a duplicate entry occurs for with the same Skeleton and Parent values, only the first will be added to the cross reference table, the second will be ignored.
### <ImbedRecurseFail>
This is a true/false element. It affects the expansion function. Setting the value to true will cause an expansion to halt if a skeleton expansion encounters a previously expanded skeleton. The following code fragments represent a valid run-time use of recursion:
Skeleton A:
⁞
)SET VAR = 1
)IM B
⁞
Skeleton B:
⁞
)SEL &VAR = 1
)IM C
)ENDSEL
⁞

Skeleton C:
⁞
)SET VAR = 2
)IM B
)ENDSEL
⁞

Because the )IM of skeleton C in skeleton B is conditional, this logic causes no problems at run time. The )IM statements work as follows:
A → B → C → B (C is not processed again due to the value of &VAR)
However, the expansion function in the skeleton analysis utility does not know the run-time values of variables. To the expansion utility, the )IM B in skeleton C could cause an infinite recursion:
A → B → C → B → C → B → …
<ImbedRecurseFail>true</ImbedRecurseFail> generates an error when the second )IM of skeleton B (marked red) is encountered.
If <ImbedRecurseFail>false</ImbedRecurseFail> is specified, then the expansion continues, however the expansion will not include the second )IM of skeleton B. Therefore any logic relative to C imbedding B will not be evident.
### <DebugInputLine>
This is a true/false element. Setting the value to true will cause the input skeleton line to be written to the CSV and XML files. This element has no effect on the fixed format file output. Note that this is not needed, but may be requested as documentation if you find that one or more skeleton lines are not being parsed correctly.

## Creating Different Run Time Versions
When creating files that will be loaded into relational databases, the ConfigurationNumber or the ConfigurationName can be used to distinguish between the cross-reference data for different PDS concatenations. There must be one configuration XML file for each set PDS concatenation that you wish to define. You must change the ConfigurationNumber and/or ConfigurationName in each XML input file that you process.
Sample batch .CMD files have been supplied showing how the utility is invoked. The Samples directory also contains files written in REXX showing how to invoke the parser from REXX. You must have a REXX interpreter installed on your system to use these files. The samples were tested with Regina REXX, which is a free, open source implementation of a REXX interpreter.
## The Graphical Front-End
The graphical front-end (GFE) can be used to pass an XML configuration file to the parser engine. This configuration file is not required to generate any of the output files (CSV, XML, fixed format) normally created in the batch run of the parser. The GFE invokes the parser engine and then uses the transient intermediate data objects created by the parser as relational data.

When the ISPF skeleton analyzer is installed, the GFE is added to the Start Menu's program items under the name “Skeleton Parser Query Program”:

Each time you run the program, it will prompt for a configuration XML file:

The file you select is validated. Then the skeleton files in the folders specified in the <Directory> entries in the XML file are scanned. The cross-reference information is placed in transient tables, internal to the program.
Following the scan the query program's home dialog is displayed:

<Display> name from the XML configuration file.
Display the Skeleton-to-Variable cross-reference table

Display the Skeleton-to-Skeleton cross-reference table.

Select a new XML configuration file.

Display the Skeleton-to-Table (DOT) cross-reference table

Select a skeleton to expand.

Display the Skeleton-to-Executed program cross-reference table.

Expandthe skeleton named in the drop-down selection box.

### Load a New Configuration

The New Configuration button allows you to browse for a new configuration file. The skeletons indicated by the new file will be scanned. Any prior data relationships will be deleted. The internal transient tables will be loaded with new data relationships.
If any of the queries (Skeleton-Skeleton, Skeleton-Variable, Skeleton-Table, Skeleton-Program or the Skeleton Expansion) are open, you will be prompted to either close them and load and parse skeletons from a new configuration or to cancel and return to using the current configuration with the already parsed skeletons.
### Skeleton to Variable Cross-Reference

The Skeleton-Variable button displays the Variable cross-reference Panel:

Filters
Sorting
Filter Execution
Filter Discontinue

When the table is first displayed, all variables of all reference types in all skeletons are displayed. You can filter the results by selecting a particular skeleton and/or variable and/or reference type; then push the “Filter” button. Here are the results filtered by a specific skeleton:

Note that the sort order was changed by selecting the Order By drop down and choosing “Skeleton Name, Line Number”. There are three ways the data can be sorted:

It is not possible to select multiple skeletons or variable names when filtering the data. But you can have multiple instances of the cross-reference dialog open simultaneously. Each can be separately filtered.
To discontinue filtering, simply press the “All” button.
#### Exporting data

There are three data export functions. The first Export menu item on this form is Export CSV... Select the export to create a comma separated value file of the currently active data. This file can be loaded into a spreadsheet or database:

The second Export menu item Export XML... is used to export the currently active data as an XML data file.
The last Export menu item Export CSV 1-1... is used to export a comma separated value file containing only the skeleton and variable names in a one-to-one relationship. This can allow you to document variable usage within a skeleton. Once you manually update the exported data with your comments, you should not export to that CSV again, or you will wipe out your updates.

### Skeleton to Skeleton Cross-Reference

The Skeleton-Skeleton button displays the Skeleton cross-reference panel:

Filter

Filter Execution

Filter Discontinue

When the table is first displayed, all skeletons that imbed other skeletons are shown along with the skeletons they imbed. You can filter the results by selecting a particular skeleton; then push the “Filter” button. Here are the results filtered by a specific skeleton, CMN$$MFS:

Note that the filtered skeleton cross-reference shows all the skeletons that issue )IM for CMN$$MFS as well as those skeletons for which CMN$$MFS issues )IM's.
Columns:
Skeleton	This is the imbedding (parent) skeleton.
Offset	The PDS in the concatenation where the member is located.
Line	The line in the parent skeleton where the )IM statement was found
Imbedded	The imbedded (child) skeleton
ImbedOffset	The PDS in the concatenation where the imbedded member is located. If the value is -1,	then the imbedded skeleton does not exist in the concatenation.
EXT	If the )IM statement contains the EXT (extensions) option, this box will be checked
NOFT	If the )IM statement disables file tailoring (the NOFT option) for the imbedded skeleton,	this box will be checked.
OPT	If the )IM statement indicates that the imbedded skeleton is optional (that is no error will	occur if the )IM'ed skeleton does not exist), then this box will be checked.
#### Exporting data

There are three data export functions. The first Export menu item on this form is Export CSV... Select the export to create a comma separated value folder of the currently active data. This file can be loaded into a spreadsheet or database:

The second Export menu item Export XML... is used to export the currently active data as an XML data file.
The last Export menu item Export Unimbedded exports an set of XML data lines that can be copied into the configuration file, where you can define REXX, z/OS assembly language or a higher level language program or function as the parent for skeletons that are not imbedded by other skeletons, but rather by FTINCL from a program or dialog. The exported data looks like this:

### Skeleton to Table (DOT) cross-reference

The Skeleton-Table button displays the Table cross-reference panel:

Filter Execution
Filter Discontinue
Filters

When the cross-reference is first displayed, all skeletons and table loops (DOT) are shown. You can filter the results by selecting a particular skeleton and/or table; then push the “Filter” button. Here are the results filtered by a specific skeleton, CMN$$LNK:

Columns:
Skeleton	This is the imbedding (parent) skeleton.
Table	The table name. Note: Tables with names containing variables are also shown, if they	exist.
Line	The line in the skeleton where the )DOT statement was found
#### Exporting data

There are two data export functions. The first Export menu item on this form is Export CSV... Select the export to create a comma separated value folder of the currently active data. This file can be loaded into a spreadsheet or database:

The second Export menu item Export XML... is used to export the currently active data as an XML data file.
### Skeleton to Program Cross-Reference

The Skeleton-Program button displays the executed program cross-reference panel:

Filter Execution
Filters

Filter Discontinue
When the cross-reference is first displayed, all skeletons and executed program names are shown. You can filter the results by selecting a particular skeleton and/or program name; then push the “Filter” button. Here are the results filtered by a specific skeleton, CMN$$LNK:

Columns:
Skeleton	This is the imbedding (parent) skeleton.
Program	The executed program name. Note: Programs with names containing variables are also	shown, if they exist.
Line	The line in the skeleton where the )DOT statement was found
#### Exporting data

There are two data export functions. The first Export menu item on this form is Export CSV... Select the export to create a comma separated value folder of the currently active data. This file can be loaded into a spreadsheet or database:

The second Export menu item Export XML... is used to export the currently active data as an XML data file.
### Skeleton Expansion

The skeleton expansion function operates on the skeleton indicated in the drop down selector on the home form. The expansion processes each )IM statement in the main file, adding the imbedded skeleton to the expansion. When an imbedded skeleton has an )IM statement, the skeleton associated with that statement is processed.
The result is placed in a viewable, scrollable table:

Variables and/or constants referenced on the highlighted line
The skeleton commands that were in effect to reach the selected line.

The selected (current) line.
Columns:
Skeleton	The skeleton currently being processed.
Offset	The relative offset of this line from the start of the expansion
LineNo	The offset of the line in the skeleton
This data is followed by the actual line from the skeleton.

#### Expansion Context Menu
##### Filtering Text Within a skeleton line
The expansion grid has a context menu for filtering the displayed lines or for moving to a specific line in the expansion:

The context menu is activated by positioning the mouse pointer in the main expansion grid and clicking on the right mouse button.
The Filter...Text in Line... selection allows you to specify a character string to find:

Filtering for )IF finds all lines with )IF somewhere in the text. Then only those lines are displayed:

##### Using a Filter to Hide Skeleton Expansions
There is a second filter type, used to hide a skeleton in the expansion. One or more skeletons can be hidden to allow easier analysis of lines:

As shown, you may select multiple skeletons in a single request. You can also make multiple requests, hiding more skeletons.
The above filter has the result shown below. Note that after the )IM of SKM$$VAR on line 3, that 1019 lines of SKM$$VAR are suppressed. Also note that in the Status area at the bottom of the form, that there is now a drop down box titled “Hidden skeletons (Drop down to list)”.

After the drop down is clicked, the list of hidden skeletons is shown.

##### Removing Filters
Once any filter has been applied, the Remove Filters... context menu item is enabled:

You can remove the active text filter (in this case the filter is on “)SET”). You can also remove any or all skeleton filters. The first skeleton hiding filter removal menu item is for picking one or more hidden skeletons to remove. The next skeleton hiding filter removal menu item redisplays all skeletons.
The “Remove all filters” selection redisplays all skeletons in the expansion, as well as removing the text filter.
There is one additional way to redisplay a hidden skeleton. Using the “Hidden skeletons” drop down list, you can select any of the skeletons in the list. This will redisplay the selected skeleton.

##### Positioning on a Specific Line (Goto)
You can view lines in the expansion grid by clicking on the Offset and End-Offset cells in the Skeleton Logic grid. The expansion grid will display the line referenced in the cell you clicked on. If possible, a few lines above the selected line will also be displayed, so that the line may be a few lines down. You may notice in some cases that the grid will be displayed with the indicated line at the top. You may also use the Go to line... context menu item to reposition the grid to a specified. Neither the Go to line... context menu item nor the Skeleton Logic Offset/End-Offset click will change the current row pointer.

Select a line in the list of commands active for the current line (189).

The current line in the expansion will remain 189 and the Skeleton Logic grid will remain unchanged.

Notice that the selected line is still line 189 and that the “Skeleton logic” area has not changed. But the Go to line... has positioned the grid so that the selected line is now displayed. In this example, you can return to line 189 either by using the Go to line... context menu item and either specifying the line number 189, or by leaving the line number blank, or by simply clicking in the Offset cell in the first line of the Skeleton Logic grid.. The Go to line... is not limited to the lines in the logic grid.
To make the Go to line... target line the current line, simply click on the line when it is displayed.
#### Skeleton Logic Display For A Selected Line
When a line is selected by clicking on it the table on the lower left will show the ISPF Skeleton commands: )SEL/IF/ELSE/DO/DOT/IM that were in effect when this line was encountered. The table has the label Skeleton logic leading to the selected line. By clicking with the left mouse button in any line within this table the Expansion table view changes to show that line and two lines preceding and the lines that follow the selected line. Changing the view does not change the selected line, so the skeleton logic table remains unchanged. You can quickly return to the selected line by clicking on the top line in the skeleton logic table.
The left mouse button click functionality of the Skeleton logic... table is disabled when the line filter is activated in the expansion grid.
#### Variables Display Within Lines
The table on the lower right will show the variables and constants referenced on that line. This table has the label Variables on the selected line. If you double click a line in this table, a Skeleton-Variable cross-reference form will open showing all the skeletons that use the variable or constant:

#### Graphic View
On the expansion form there is a button labeled “Graphic View”. Press this button to show the relationships among all of the )IM'd skeletons in an expansion: